## Slide 1: PerfVec: Generalizable Performance Modeling using Learned Program and Architecture Representations
SIGMETRICS 2025
Stony Brook, NY
Lingda Li, Sairam Sri Vatsavai, Kuan-Chieh Hsu
Brookhaven National Laboratory

## Slide 2: Agenda
PerfVec overview (30 mins)
Performance prediction demo/hands-on (30 mins)
Design space exploration (15 mins)
Source code (5 mins)
Open discussion (10 mins)
Repository: https://github.com/PerfVec/PerfVec
  Source code and other materials used in this tutorial

## Slide 3: PerfVec Overview

## Slide 4: Performance Modeling for Computer Architecture
Essential to computer architecture research and engineering
  New design evaluation, design space exploration, resource scheduling, …
Goals: speed, accuracy, and generalizability
Methodology | Speed | Accuracy | Generalizability
Analytical Modeling | Fast | Low | High
 |  | High | Low
Discrete Event Simulation | Slow | Variable | High
Emulation | Medium | Variable | Medium
Machine Learning (ML)-based Modeling | Fast | High | Low
ML-based Simulation | Medium | Variable | Medium
Goal: explore better tradeoff using ML, especially on generalizability
PerfVec (this work) | Fast? | High? | High?

## Slide 5: Generalizable Performance Modeling
Performance is determined by both software and hardware.
A generic performance model should separate the impact of software (program) and hardware (microarchitecture).
  When one changes, no need to re-model the other
Not trivial to achieve such separation
  Complex interplay between program and microarchitecture
  Several analytical models tried to do it manually.
PerfVec learns the separation automatically.

## Slide 6: Learning Separation
The same program representation is used to predict its performance on any microarchitecture, and vice versa.
Key idea 1: have two independent ML models to capture the performance impacts of program and microarchitecture, respectively
independent
of each other
Focus of this work

## Slide 7: Learning Program Representation
Challenge: programs typical execute at least billions of instructions, and no ML model can deal with such long sequences.
Input | Level of Detail | Limitation
Profiling info (e.g., performance counters) | Low | Often microarchitecture dependent Lack of low level details
Static program info (e.g., control flow graph) | Medium | Cannot capture dynamic execution (e.g., input impact) Huge graphs to learn from
Instruction execution trace | High | Huge amounts of instructions to learn from
Key idea 2: 1) learn the representations of individual instructions and 2) compose a program representation from those of all its executed instructions (divide-and-conquer)

## Slide 8: Learning Instruction Representation
Performance determination factors of an instruction
Factor | Microarchitecture Independent Feature
Own properties | Static properties (e.g., operation type); dynamic behavior (e.g., branch direction); reuse distance; branch entropy
Co-running instructions | Co-running instructions’ properties
A sequence model
(e.g., LSTM, Transformer)
Refer to the paper on how to compose program representation
Generalizable across programs
Program traces are different sequences of instructions from the same set.
Instruction
representation
model
Instructioni’s representation
Instructioni’s features
Instructioni-1’s features
…
Instructioni-c’s features
Instruction1’s representation
…
Instructionn’s representation
…
Program representation

## Slide 9: PerfVec Training
Train representations of sampled microarchitectures jointly
Natural solution: training all models end-to-end
Challenge
  Irregular and alterable microarchitectural space
  Difficult to train a universal microarchitecture representation model
Hypothesis: training with a sufficient number of diverse microarchitectures enables generalizability to others.
Key idea 3: train the instruction representation model to predict instruction latencies on randomly selected microarchitectures for generalizability
Replace the program representation model

## Slide 10: Data Acquisition & Model Architecture
Instruction traces from gem5 simulation
  Easy to obtain instruction level latency
  Easy to configure microarchitectures
Programs
  17 SPEC CPU2017 benchmarks
  10 for training, 7 for testing
Microarchitectures
  Randomly generated gem5 configurations
    In-order/out-of-order cores, caches, memory, etc.
  77 for training, 10 for testing
Model architecture
  2-layer LSTM by default
  See the paper for other architectures

## Slide 11: Generalizability Evaluation
Prediction error range against gem5 simulation across all microarchitectures
Unseen microarchitectures
Unseen programs
The trained model generalizes well to unseen programs and microarchitectures.

## Slide 12: PerfVec Summary
High generalizability
  Learn independent program and microarchitecture representations
Good accuracy
  Learn program representations from instruction execution traces
Fast speed
  Simple combination of program and microarchitecture representations
Many potential applications
  Design space exploration, performance analysis, …
Code: https://github.com/PerfVec/PerfVec

## Slide 13: Performance Prediction Demo/Hands-on

## Slide 15: Design Space Exploration

## Slide 16: PerfVec Use Cases
Performance modeling is essential for many tasks.
  PerfVec can be used in them.
A case study: design space exploration (DSE)
  Find the optimal design(s) given one/multiple objective function(s)
DSE example: L1 and L2 cache size exploration
  Objective function: execution_time * (1000 + 10*L1_size + L2_size)
    Similar to latency area product
  Select the best cache sizes for 17 SPEC CPU2017 benchmarks

## Slide 17: DSE Procedure
Froze during training
Train a microarchitecture representation model
Training data: gem5 simulation traces of 3 benchmarks on selected configurations
Predict the performance of all benchmarks
  Use the trained microarchitecture representation model and existing program representations
A 2-layer MLP

## Slide 18: DSE Results
  Complete gem5 simulation: 600 hours
  Previous ML-based DSE methods
  Use selected simulation results to train program-specific models
  Need to simulate many configurations for each program
  PerfVec
  Incur significantly less overhead with comparable quality
  11 hours = 5 (data collection) + 6 (training)
Ïpek et al. Efficiently exploring architectural design spaces via predictive modeling. ASPLOS 2006.
Dubach et al. Microarchitectural design space exploration using an architecture-centric approach. MICRO 2007.
Li et al. Efficient design space exploration via statistical sampling and adaboost learning. DAC 2016.
Overhead: the time to construct models (hours)
Quality: how close the selected design is to the optimal design.
Lower is better
Method | Overhead | Quality
ASPLOS06 | 150 | 4.4%
MICRO07 | 84 | 4.7%
DAC16 | 170 | 3.6%
PerfVec | 11 | 3.6%

## Slide 20: Source Code

## Slide 21: Top Level Folders
DP: data processing scripts for simulation traces
  Implemented using Python (NumPy) and C++
ML: scripts for training, test, models, etc.
  Implemented using PyTorch
CFG: configuration files for datasets
Tutorials: descriptive instructions and documents
DA: data analysis scripts

## Slide 22: ML Folder
models: neural network architectures
  LSTM, Transformer, CNN, MLP, …
train.py: train instruction representation models
test.py: test prediction accuracy of trained models
tune.py: fine-tune microarchitecture representation models and representations
custom_data*.py: data loaders for PerfVec datasets

## Slide 23: DP Folder

## Slide 24: Open Discussion
Questions?
Comments?
Collaboration opportunities?